## Slide 1: UNDERSTANDING TESLA POWERWALL ECONOMICS
…The search for a positive return
Eric Scott, 3/25/16

## Slide 2: Quick Background: 1991-2011
From Toronto, Canada
McMaster University, Mechanical Eng and Management
Manufacturing engineering intern @ Linamar
Notes: -Mcmaster is a public research university in Hamilton ontario
-one of canada’s top schools
-mech eng and management – dual degree mechanical engineering and business (5 year program)
Linamar is one of Canada’s largest manufacturing companies, primary focus on automotive
-worked as a manufacturing engineering intern assisting project engineers
-manufactured camshafts, connecting rods, and cyclinder blocks for GM, Ford and Chrysler

## Slide 3: 2011-2014
Shifting focus to research / environment
Numerical modeling @ Environment Canada
Research assistant @ National Institute of Nanotechnology
Notes: Environment canada is the research division focusing on metrology and ato
The National Institute for Nanotechnology is a research institution located on the University of Alberta main campus, in Edmonton
-worked for a mechanical engineering professor in the summer – working to commercialize research from one of his PhD students
-created a 3D strain sensor, typical strain sensors only give you planar information (2D) - this used semiconductor technology to provide a 3D profile
-interest from oil&gas companies in Alberta that wanted to use it to detect leakages from pipelines
-wanted to create a network of 3D strain sensors

## Slide 4: 2014-current
Shifting focus to data & energy
UC Berkeley, M.Eng
Design Engineer @ SolarCity (9 months)
Notes: Masters at UC Berkeley graduated last May
-1 year accelerated masters, engineering and business focus
-classes offered through the Haas school as well as engineering
-capstone with Gov. Granholm – American Jobs Project
-renewable energy policy around the US

## Slide 5: Today’s Presentation Outline
Origins of the project
Initial look at San Francisco Region
Messing around with the parameters
Building a little application
Demo

## Slide 6: Sales training video
SolarCity offering Powerwalls to homeowners
10kWh (weekly cycling) model
Sales training: cost reduction is not the value proposition
Main sell point: back-up generation
Back-up generation = no-payback
Daily cycling = possible payback???
Notes: No longer offering the 10kWh battery – this was just over a month ago when I stared looking into the economics
-often here that a battery just doesn’t make financial sense - -I wanted to see to what degree??
-what factors were involved, how to go about solving a problem like this?

## Slide 7: Looking for data
http://en.openei.org/datasets/dataset/commercial-and-residential-hourly-load-profiles-for-all-tmy3-locations-in-the-united-states
Notes: Step1 in the project was to find residential energy data
-good source OpenEI is a wiki-type organization that hosts a number of energy related datasests
-resi data is based on Building America House Simulation Protocols – developed by NREL which models the house based on geographic conditions/weather/standard costruction types
-uses data from residential energy consumption survey as a statistical reference to verify the model data
-1000 different regions- all csv files referenced by a WMO ID#
-had worked with the dataset before on a previous project
-split into commercial and residential datasets
-16 commercial ‘types’ for 1000 different regions across the US

## Slide 8: SF residential data

## Slide 9: Exploring the PG&E tariffs
What does a homeowner pay for electricity?
PG&E electric schedule E-1:
http://www.pge.com/tariffs/tm2/pdf/ELEC_SCHEDS_E-1.pdf
Notes: -average price in the region ~25center/kWh

## Slide 10: San Francisco baseline
Zip code look-up
    7kWh summer, 8kWh winter
http://www.pge.com/tariffs/tm2/pdf/ELEC_SCHEDS_E-1.pdf
http://www.pge.com/en/myhome/saveenergymoney/financialassistance/medicalbaseline/understand/index.page?WT.mc_id=Vanity_baseline
Notes: -different regions have different baselines
Summer: May-Oct
Winter: November-April

## Slide 11: Aligning cost and usage
Notes: Simulating a years worth of electricty costs based on usage data
-calcualte the usage each day - %of the baseline and allocate a cost to that

## Slide 12: TOU: Utility tariff for a clean-energy grid
http://www.pge.com/tariffs/tm2/pdf/ELEC_SCHEDS_E-6.pdf
Time-of-use tariff incentivizing usage during off-peak
  PG&E E-6 schedule
Notes: Efforts by PG&E to promote a time-of-use rate tariff which charges users different amounts during times of day
-begins to break up the tiered rate structure, add more flexibility to usage patterns

## Slide 13: TOU (no battery)
Notes: -again aligned cost and usage
Total cost $1956
-more than the E-1 tiered rate, makes sense, incentivized to swtich consumption on the new rate plan so you’re slightly penalized if you don’t
-% each day of baseline, also need to track what times usage occurred? Peak/partial-peak/off-peak? – what percentage of the total? Then assign a cost to each day

## Slide 14: Building a simple battery dispatch algorithm
http://www.pge.com/en/myhome/saveenergymoney/plans/tou/index.page
charge
discharge
Notes: -nice graphic from PG&E to show the TOU rate charges
-overlayed these rectanges to show how I started to think about a battery dispatch strategy
-charge during off-peak times 1am-5am as needed until battery is full at max charging rate (1C)
-discharge –if available during the times shown as needed
-we will be able to charge – controlled
-but can we dispatch to meet the load?

## Slide 15: Powerwall assumptions
6.4kWh model (daily cycling)
5000 cycle life (~13 years)
End-of-life at 80% initial capacity (5.12kWh)
Linear capacity degradation
100% max depth-of-discharge, state of charge
3kW max power in/out, no fade
92% round-trip efficiency
Operated within recommended temp. (-20°C – 50°C)
No self-discharge, continuous operation
Static dispatch model

## Slide 16: Powerwall specifications match our SF load profile
Energy
  6.4kWh model (daily cycling)
  Max peak-time / partial-peak load: 5.9kWh
  92% round-trip efficiency ~ 6.4kWh needed
Power
  3kW continuous (3kW peak)
  Max energy requirement is 1.98kWh
  Assumed constant power over 1hr
    realistic assumption?
Notes: Max load being offset was 5.9kWh
-tracked this in the TOU model with no battery to find the max for the entire year’s
Energy capacity fits with this requirement
Power requirement fits only if we assume a constant power requirement
-the load data is in hourly bins -- major limitation here
-we could see spikes greater than 3kW if we had higher resolution in the data
-for the sake of this project though I assumed it was constant at the hourly-rate

## Slide 17: SOC
Notes: Building the battery into the TOU model from before
-tracked battery SOC, charged it during the morning hours and discharge during the times mentioned before to offset cost (if capacity is available in the battery)

## Slide 18: SOC sample
Notes: -January(winter) – 5 day cycling (Monday-Friday) for partial peak pricing from 5pm-8pm in the eveing
-July (summer) – 7 day cycling (Sunday-sunday) for peak pricing from 1-7pm M-F, and 5pm-8pm on the weekends
Intuitive sense, less usage on weekends although we’re still draining same time period as winter, the SOC is higher in the summer

## Slide 19: TOU (with battery)
Notes: More spikes and dips in usage, total energy actually higher than before due to the 92% battery efficiency
-dips = when we use battery energy, lower charge from grid,

## Slide 20: Battery reduces cost ~$1 - $1.50/day
Notes: Comparing the cost from before, the battery reduces dailiy charge (when it’s used) by about 1-1.50 per day
-good way to think about it
-save about $300 per year?

## Slide 21: Net Present Value Analysis
Initial investment (Co): $5500
  Battery: $3000
  Inverter/BOS: $1500
  Install costs: $1000
Cash flows are electricity cost savings
  Annual cost on E-1 – E-6 w. battery
10% project discount rate
2% utility price escalation rate
Project life is battery life (5000 cycles ~ 13 years)
No incentives/rebates
No taxes, no depreciation/salvage value, no O&M cost
Notes: Financial assumptions
-can’’t just look at 1 year, need to see for the entire year of the battery
-compare the standard E-1 schedule with the E-6 rate + battery

## Slide 22: No positive payback for Powerwall in SF
Notes: REUSLT, given standard assumptions, battery in SF region of CA does NOT make financial sense for residential customers
--
No PV included
-if we consider the case of a homeowner with PV – they can use the battery to USE more PV energy
-BUT still, the current tariff structure as NEM – so excess energy is backfed onto the grid at retail rate
-doesn’t make sense to want to use the battery because you lose energy through eff. loss!

## Slide 23: Battery storage needs financial help
Negative NPV can be offset by:
  Incentives / rebates (SGIP program from PG&E)
  Unsustainable
Alternative revenue streams
  Pay for behind-the-meter services
  Where the grid is headed
http://www.rmi.org/electricity_battery_value
Notes: RMI paper
-battery storage when behind-the-meter can be aggregated to provide ALL GRID SERVICES
-the further downstream the better for the grid!

## Slide 24: 5% utility price escalation, 7% discount rate
Notes: Without looking into these alternative revenue streams
-I made assumptions that could be tweaked
----limitation is I approached the case from the NPV side , better might be the internal rate of return (IRR)
-instead of assuming a discount rate, we solve for the discount rate that yields a positive NPV
-can compare that to alternative projects (higher the IRR the better!)
-bond~1-2% depending on the length
Either way, play around with parameters to see what will yield a positive NPV
-played with many different scenarios, for exmaple. High cabron tax, utility price escalation goes way up

## Slide 25: What about other regions?
Different PG&E ‘territories’
Different baselines
Different load profiles
Create a tool to vary the region / parameters
Use Tkinter library in python to create a simple application
Another way to ‘play-around’ with NPV
DEMO
Notes: Utilize more of the dataset?
-how to incorporate the utility tariffs?
-stick with PG&E but alter the baselines

## Slide 26: Key learning takeaways
Visualizing the data
  Can use open datasets (OpenEI, green button, etc.)
  Finding the best way / tools to visualize energy data
Understanding the tariffs
  Different across the county
  How to build that into a model
Understanding battery limitations
  Modeling battery performance / yielding a favorable payback
Importance of battery storage for grid modernization
  Currently rely on incentives / revenue streams not yet available
  Resi v. commercial v. utility scale

## Slide 27: Questions?

## Slide 28: Backup: Information about dataset
http://en.openei.org/datasets/dataset/commercial-and-residential-hourly-load-profiles-for-all-tmy3-locations-in-the-united-states information
About 1000 csv files
20GB
Hourly load